## Slide 1: Adding FreeRTOS

## Slide 2: FreeRTOS Documentation
Notes: Right click RTOS and Open Documentation

## Slide 3: Task Creation
Notes: Right click RTOS and Open Documentation
pvTaskCode – Function pointer
pcName – Task name
usStackDepth – how large to make the stack
pvParameters – possible to pass parameters to the task
uxPriority – Priority of the task
pxCreatedTask – pass a handle to the task for reference for the rest of the program

## Slide 4: Task Example
Notes: vTaskDelay
Delay for so many ticks

## Slide 5: Queue Creation
Put QueueHandle_t xQueue variable at the top of main to reference this Queue globally.
Create the Queue
xQueue = xQueueCreate( 1, sizeof( char ) );
Notes: Parameters
xQueue The handle of the queue
pvBuffer A pointer to the memory into which the received data will be copied.
xTicksToWait portMAX_DELAY will cause the task to wait indefinitely (without timing out)

## Slide 6: Queue Creation
Put QueueHandle_t xQueue variable at the top of main to reference this Queue.
Notes: Parameters
xQueue The handle of the queue
pvBuffer A pointer to the memory into which the received data will be copied.
xTicksToWait portMAX_DELAY will cause the task to wait indefinitely (without timing out)

## Slide 7: Send to Queue from ISR
Inside the USART 2 ISR
uint8_t characterReceived;
characterReceived = USART2->DR;
xQueueSendToFrontFromISR( xQueue, &characterReceived, NULL);
Notes: Parameters
xQueue The handle of the queue to which the data is being sent (written).
pvItemToQueue A pointer to the data to be copied into the queue.
pxHigherPriorityTaskWoken From FreeRTOS V7.3.0 pxHigherPriorityTaskWoken is an optional parameter and can be set to NULL.

## Slide 8: Application Example
Blinky Task
CLI Task
USART2 ISR
Notes: vTaskDelay
Delay for so many ticks