## Slide 1: ENSE 452
Timer 2 and USART Interrupt

## Slide 2: STM32 Clock Tree

## Slide 3: STM32 Clock Tree
Since the CPU clock is 72MHz and APB1 clock is 36MHz, the prescaler for APB1 is set to 2. So if the APB1 prescaler =2 then the clock to the general purpose timers (Timer 2) is:
36MHz x 2 = 72MHz

## Slide 4: Timer Registers of Interest
APB1_ENR – Peripheral Clock Enable Register
TIMx_CNT – Counter Register
TIMx_PSC – Prescaler Register
TIMx_ARR – Auto-Reload Register
TIMx_CR1 – Control Register 1
TIMx_SR – Status Register

## Slide 5: Polling vs Interrupt
  Polling
  Ties down the CPU
  CPU services the device
  Inefficient
  Interrupt
  Hardware Mechanism
  Interrupt handler works with the device
  Saves CPU cycles

## Slide 6
  NVIC – Nested Vector Interrupt Controller
Interrupt in Cortex-M

## Slide 7
  Interrupt Vector
Interrupt in Cortex-M

## Slide 8
Enabling Peripheral Interrupts
  To use the function include “stm323f10x.h”

## Slide 9
Enabling USART Interrupts

## Slide 10
Interrupt Service Routines Best Practices
  Keep them short and sweet
  Global variables – be careful
  Calling functions in ISR’s - not recommended
  Indicate that the interrupt has been serviced when done